## Slide 1: Analyzing Sub-threshold Bitcell Topologies and the Effects of Assist Methods on SRAM Vmin
By: James Boley

## Slide 2: Benefits of Sub-threshold (VDD<VT)
Sub-threshold benefits: VDD from [1.8,1.0]V to [0.4,0.2]V
Leakage Power Decreases: Power = VDD Ioff
VDD goes down: 2.5X to 9X
DIBL reduces Isub-threshold: 2X to 10X
Pleak: 5X to 90X
Energy Consumption Decreases Aging Effects Improve
Eactive = CVDD2 NBTI, EM, TDDB
Etotal/operation minimized in sub-VT
Main Limitations: Variation, Slow Speed

## Slide 3: Sub-Threshold SRAM
Familiar Problems
  Hold static noise margin (SNM), Read SNM, Write SNM
New Problems:
  Conventional 6T bitcell becomes unreliable below ~700 mV
  Reduced Ion/Ioff ratio (Read access failure)
  Exaggerated VT variation impact (Ion varies exponentially with VT)
Solutions
  Use more area (8T & 10T bitcells)
  Read SNM: Use a read buffer
  Write SNM: Use write assist (Boosted WL/Negative BL VSS)
  Read Access: combination of assists
Observation: Problems faced by subthreshold SRAM are very similar to what normal SRAM will encounter in two or three generations
[*Ref: J. Ryan, J. Wang, B. Calhoun, GLSVLSI’07]

## Slide 4: Outline
Introduction of Sub-threshold Bitcell Topologies
Overview of Assist methods
Introduction of Test Chip and Results
Conclusion

## Slide 5: Outline
Introduction of Sub-threshold Bitcell Topologies
Overview of Assist methods
Introduction of Test Chip and Results
Conclusion

## Slide 6: Non-6T Cell for Read Stability
[J. Kulkarni, JSSC’07]
Schmitt-trigger (ST-cell)
RWL
QB
RBL
BufFoot
8T-cell
[L.Chang, VLSI’05]
[N. Verma,ISSCC’07]
8T Buffer decouples read operation, therefore the Read SNM becomes the Hold SNM
10T ST-cell- NR2/NFR weaken PD network when VR=1, increasing switching threshold of right inverter
NL2
NR2
NL1
NR1
NFL
NFR
XL
XR
PR
PL
VL=0
VR=1
VDD
VDD
VNL
VNR
VDD
WL
BL
BLB
NL1
NR1
XL
XR
PR
PL
Q=0
QB=1
VDD
WL
BL
BLB

## Slide 7: Read Stability Comparison for Sub-VT bitcells
6T Read 3σ
6T Read u
6T Hold u
6T-cell costs too much area for better read SNM
8T cell has the best read SNM, which is same with 6T hold SNM
ST Hold u
ST Read u
ST Read 3σ
ST Hold 3σ
ST-cell has the best hold SNM, but its read SNM is not as good as 6T hold SNM
6T Hold 3σ, 8T READ SNM
Use a buffer to fix Read SNM

## Slide 8: 8T Asymmetric Schmitt Trigger Bitcell
Uses single-ended reading and asymmetric inverters similar to the 5T cell described in [Nalam, CICC’09] to increase read margin
Write operation similar to 6T write
Asymmetric ST cell achieves 86% higher static read noise margin (RSNM) than the 6T cell, and 19% higher RSNM than the 10T ST cell
TL
PL
NL
TR
PR
NR1
NR2
NF
VDD
WL
BLB
BL
WWL
10T ST
6T
Asym ST

## Slide 9: Outline
Introduction of Sub-threshold Bitcell Topologies
Overview of Assist methods
Introduction of Test Chip and Results
Conclusion

## Slide 10: Improve Write NM
Goal
  Weaken pull-up FET
  Strengthen pass-gate FET
Knobs
  Size pass-gate to pull-up ratio (not efficient)
  Collapse VDD to weaken PFET
  Boost WL VDD
    Cons: half selected cell stability
  Reduce BLVSS
    Cons: increased BL leakage
RWLon>VDD
BL<VSS
PG
PU
PD
VGSPG>VDD
‘1’
‘0’

## Slide 11: Improve Read Access/Stability
Keys
  Increase Ion
  Reduce Ioff (BL leakage current in unaccessed cells)
Knobs
C. boosted bitcell voltage
D. negative bitcell VSS
RWLoff<0
QB
RBL
B: negative off-WL
A: boosted on-WL
Ioff
RWLon>VDD
QB
RBL
Ion
Note: while negative bitcell VSS results in only slight improvements in RSNM, it significantly reduces read delay due to the body effect strengthening both the pull-down and pass-gate transistors
[R. Mann, ISQED’10]

## Slide 12: Outline
Introduction of Sub-threshold Bitcell Topologies
Overview of Assist methods
Introduction of Test Chip and Results
Conclusion

## Slide 13: 180nm SOI Test Chip
Each array contains two 4Kb banks
128 rows x 2-16 bit words
6T & 8T iso-area: 24 um2
ST & Asymmetric ST iso-area: 32 um2
  33 % area penalty vs. 6T
Peripheral and bitcell array voltages controlled by separate supplies
Fabricated on MITLL 180nm FDSOI technology
6T Array
8T Array
10T STn
Assym STn

## Slide 14: Data Retention Voltage (DRV)
Non-ideal yield
  First run of a new technology
  Full columns non-functional
  Random bit failures
Large die to die variation
  On chip 2: 80% of bits retained their value down to 255 mV compared to only 16% on chip 1
Overall 6T has marginally better DRV
Dead Columns
Chip 1
Chip 2
Random bit failures

## Slide 15: Read and Write Vmin without assists
SRAM write limited
  Best Case write Vmin at 80% yield is 620 mV with the Asymmetric ST cell
  Best Case read Vmin at 80% yield is the 8T cell at 440 mV
The 8T cell offers the lowest Read Vmin, which is surprisingly only 10% lower than the 6T and Asymmetric ST bitcells

## Slide 16: Observations
All bitcells have similar read and write Vmin
  RSNM of the Asymmetric ST and 10T ST in simulation was much higher than the 6T
Discrepancy between spice models and silicon data
  Transistor sizing more sensitive in simulation than on silicon
Low yield for relatively small SRAM array
  First run of a brand new technology
  Still able to see trends with the assist methods

## Slide 17: Write Assists
BLVSS = -100 mV
  At 80% yield Vmin is reduced:
  30% 6T/Asym Schmitt Trigger
  27% Schmitt Trigger
  23% 8T
WLVDD boosted 100mV
  At 80% yield Vmin is reduced:
  18% Schmitt Trigger
  12% 8T
  7% Asymmetric Schmitt Trigger
  3% 6T
190 mV reduction of Vmin at 80% yield
110 mV reduction of Vmin at 80% yield

## Slide 18: Read Assists
Reducing WLVSS and CVSS consistently improved read Vmin for each of the cells
  Suggests that bitline leakage was a major contributor to reduced read margin
Increasing CVDD had the greatest impact on the 10T ST cell
Boosting WLVDD improved 8T
100 mV reduction of Vmin at 80% yield

## Slide 19: Write Assists – Increasing ΔV
Vmin at 70% Yield
Vmin continues to scale down as WLVDD is increased for the 8T and 10T ST cells
Reducing BLVSS below -150 mV has negligible effects on reducing Vmin
Using a combination of the 6T cell and negative BLVSS is the most area efficient strategy for reducing write Vmin

## Slide 20: Read Assists – Increasing ΔV
Increasing WL VDD/VSS from 100 mV to 200 mV has no effect on Read Vmin
Reducing CVSS below 100 mV has negative effect on Vmin
Increasing CVDD beyond 100 mV results in a 14% reduction in Vmin for the Asymmetric ST bitcell

## Slide 21: Conclusions
Although the Asymmetrical ST and 10 ST bitcells showed higher RSNM in simulation, silicon results showed Read Vmin comparable to the 6T bitcell
Subthreshold bitcells proved to be write limited- unassited write Vmin 41% higher than read Vmin
BLVSS reduction is the most effective write assist method reducing the Vmin by 46% at -200 mV
WLVSS reduction was able to reduce Read Vmin up to 25%
Using assist methods was more effective at reducing Vmin than designing new bitcells

## Slide 22: Thanks!
Any Questions?